## Slide 1: Wireless Mesh Networks and their Applications
Colter Roche

## Slide 2: What are Mesh Networks?
Decentralized, self organizing networks of devices
Devices on the network serve as access point and router
Nodes can be added or removed at any time, and the network will adjust accordingly

## Slide 3: How are mesh networks used?
Mesh networks are used to connect varying numbers of devices together
Sensor arrays for managing industrial applications
Connecting smart lightbulbs, door locks and thermostats in smart home setups
Military and emergency communications in remote locations
Expanding internet coverage in areas without internet infrastructure

## Slide 4: A Brief history
Packet radio systems were created to link the Hawaiian Islands in case of emergency
DARPA created a wireless version of ARPANET, the precursor the internet
Mobile Ad hoc Networks (MANET) were developed in the 90’s, allowed for networks of devices but do not support fixed base stations
Wireless mesh networks are a subset of MANETs that DO allow for stationary nodes as well as mobile nodes

## Slide 5: Routing Protocol Types
Table driven routing (OLSR and B.A.T.M.A.N.)
  Nodes keep a routing table with paths to other nodes on the network
On demand routing (ABR and DSR)
  Paths are determined dynamically when information needs to be transferred
Hybrid routing (ZRP)
  A proactive table system is combined with a reactive on demand system
Hierarchical routing (FSR and OrderOne)
  Nodes are organized into a tree and paths are determined based on that
ZigBee
  Multi-level mesh protocol with custom chips and radios
  Used for low-power, low-cost sensor networks and smart home applications

## Slide 6: Table Driven Routing Protocols
The Optimized Link State Routing Protocol (O.L.S.R.)
  Assigns certain nodes to be Multipoint Relays (MPRs) in charge of keeping routing data
  MPRs periodically send control messages to the rest of the network to update the routing tables
  OLSR has less delay and less issues with control messages due to the periodic sending of messages, but fixing broken paths is slow and keeping tables up to date has high overhead
The Better Approach to Mobile Ad Hoc Networking (B.A.T.M.A.N.)
  Nodes only store information about where they received packets from, and then pass that information on to adjacent nodes only
  Directional information is spread across the network, and when a packet is sent, the path is dynamically generated from each node’s info on adjacent nodes
  Link fixing is much faster than OLSR for this reason

## Slide 7: On Demand Routing Protocols
Associativity Based Routing (ABR)
  Uses a three step process to route data without storing information about the whole network in tables
  Only stores routes currently needed, and deletes the record after it grows stale
  Routes are generated by sending a packet to find the destination, and then sending a confirmation back by the shortest path. That route is then stored in the tables of nodes along the path
  If a link is broken, the last functional node before the break performs the exploratory packet step from there
Dynamic Source Routing (DSR)
  Similar to ABR, except path information for all previous nodes are stored in the table of each node along the path
  When a node is lost, all this information must be purged from the tables, introducing a lot of overhead in larger networks. Route discovery also takes a long time in large networks, making DSR unsuitable in those use cases

## Slide 8: Hybrid Routing Protocols
Zone Routing Protocol (ZRP)
  Segments nodes into overlapping zones containing all nodes within a certain radius
  Nodes within zones keep routing tables for the other nodes in the zone
  Routing between zones is handled dynamically
  Updates to the routing tables only happens within zones
  Checking whether a node exists within a zone only requires checking the lookup table, allowing for larger networks and relatively low overhead
  There aren’t clear methods for selecting zone radius or having different sizes of zones

## Slide 9: Hierarchical Routing Protocols
Fisheye State Routing (FSR)
  Each node keeps a routing table tracking the location and path to surrounding nodes
  FSR periodically updates the routing table, but information on nodes further away is updated with less frequency. This leads to fuzzier information on the edges, similar to the lower amount of detail towards the edge of a fisheye lens. Route computation uses Dijkstra's algorithm.
  The lack of information for distant nodes doesn’t affect routing because each node visited along the path has up to date info on its neighbors
  FSR was not publicly released as a fully functional protocol, but it serves as a base for other protocols including OLSR
  Node disconnection can lead to temporary loops when tables have conflicting information. These loops also happen in OLSR

## Slide 10: Hierarchical Routing Protocols cont’d.
OrderOne
  A proprietary, licensed routing protocol based partially on FSR
  Nodes choose a parent node based on how dense the nodes are in that direction, and eventually a tree is formed with one or more root nodes
  Root nodes keep a routing table with paths to every other node in the network
  When a node needs to send a packet, the packet is sent to the root node and routed from there. Non-root nodes do not keep any routing information besides which node is the parent.
  Networks can be much larger than other protocols, and node power levels can vary. Since non-root nodes don’t need to maintain a table, sensors and low power nodes can be used alongside higher power node types
  Root nodes must have the memory capacity to store routing tables containing path information for all other nodes on the network, however.

## Slide 11: ZigBee Standard
ZigBee is a low-power, low-cost, multilayer protocol and hardware standard for short range IoT and sensor networks
Range is limited, but networks can be connected over the internet through ZigBee routers
Central hub required for routing
Highly secure and reliable
Requires special chips and hardware, but is very inexpensive

## Slide 12: Advantages and Disadvantages to Mesh Networks
Mesh networks are designed to be flexible and able to support devices connecting and disconnecting
This allows for infrastructure free communications networks, but introduces technical complications
Larger networks suffer from high latency and issues rerouting paths when nodes disconnect
Networks are open by design, which weakens them and can lead to exploitable vulnerabilities
Power and processing consumption for some protocols can be quite high, making mixed use networks that combine high and low powered devices more difficult

## Slide 13: Areas for future development
New protocols that can verify the position and identity of nodes are in development to combat routing based attacks
More advanced node linking with greater redundancy can reduce the time it takes for the network to establish new routes